## Slide 1
Energy research team
October 2026
Global Power Annual
Report 2025
Clean power met all new demand
Notes: This report draws on public data from Ember, the IEA, China's National Energy Administration and National Bureau of Statistics, the China Electricity Council, BNEF and others to review what happened to the world's and China's power systems in 2025, and what to watch in 2026. Global generation figures all come from Ember. Where the IEA reads the year differently, we say so. Every 2026 figure is marked as year-to-date or a forecast. Ember puts the headline this way: outside a major global downturn, fossil generation stopped growing for the first time.

## Slide 2
Clean power met all new demand.
Not settled yet.
Global demand growth
849
TWh, +2.8%
Clean power growth
887
TWh, 636 of it solar
Change in fossil power
−38
TWh, power emissions flat
Source: Ember, Global Electricity Review 2026 (Apr 2026). 2025 against 2024
Notes: This is the report's conclusion. In 2025 global electricity demand rose by 849 TWh, clean power (renewables plus nuclear) by 887 TWh, and fossil generation fell by 38 TWh, the first year without a rise since 2020. Solar did most of the work, meeting three-quarters of demand growth on its own. China was the pivot: it added 430 GW of wind and solar and its thermal output fell. But power-sector emissions only held flat. In 2026 a gas price shock has the IEA expecting coal power to rise again, and wind and solar curtailment in China is growing. That is why we call it unsettled. The report has three parts: global, China, and 2026.

## Slide 3
01
Global: solar
carried the growth
Supply, demand and emissions in 2025
04
Clean power added 887 TWh, outpacing demand
05
Solar grew 30% and met 75% of demand growth
06
Power emissions held flat. They did not fall.
Notes: Part one is global: who met the growth in demand, how much of it came from solar, and whether emissions fell with it.

## Slide 4
1
Global: solar carried the growth
Clean power added 887 TWh, outpacing demand
TWh
+636
+205
+35
+11
−38
849
Clean power +887 TWh
Solar
Wind
Nuclear
Hydro and other
Fossil
Demand growth
Source: Ember (Apr 2026). Hydro and other includes bioenergy, derived from the clean total
Notes: Global electricity demand rose by 849 TWh, or 2.8%, in line with the ten-year average of 2.7%. Clean power, meaning renewables plus nuclear, rose by 887 TWh, more than the rise in demand. Fossil generation fell by 38 TWh, the first year without a rise since 2020. Inside fossil, coal fell 63 TWh, gas rose 36 TWh and oil and other fossil fell 12 TWh. The IEA points the same way: renewables plus nuclear grew by more than total generation.

## Slide 5
1
Global: solar carried the growth
Solar grew 30% and met 75% of demand growth
Global solar generation, TWh
256
1,333
2,143
2,778
+30%
2015
2022
2024
2025
of demand growth met by solar
75%
636 of 849 TWh
renewables' share of generation
33.8%
Coal 33.0%. The IEA sees them level
Source: Ember (Apr 2026), IEA (Apr, Jul 2026)
Notes: Solar generation rose from 2143 TWh in 2024 to 2778 TWh, up 636 TWh or 30%, enough to meet 75% of demand growth on its own. Wind and solar together met 99%. Solar overtook wind (2715 TWh) for the first time. The IEA puts the solar increase lower: 620 TWh in Electricity 2026 and about 600 TWh in the Global Energy Review 2026. Only Ember says renewables have overtaken coal, at 33.8% against 33.0%. The IEA has both at about 34%, roughly level, and in its July mid-year update expects renewables to pull clearly ahead in 2026.

## Slide 6
1
Global: solar carried the growth
Power emissions held flat. They did not fall.
Change in global power sector emissions, 2025
−0.04%
+1.7% in 2024. The IEA also finds them flat, at about 13.9 Gt
of CO2
Carbon intensity of power
458
gCO2e per kWh, 2.7% below 2024
Energy-related CO2 emissions
+0.4%
Nearly 38.4 Gt, another record
Source: Ember (Apr 2026), IEA (Feb, Apr 2026). Ember counts CO2 equivalent, the IEA counts CO2
Notes: Ember estimates power-sector emissions fell by 6 MtCO2e, or 0.04%, which is effectively flat, after a 1.7% rise in 2024. China fell 37 Mt and India 42 Mt, the first time this century both fell in the same year. But the US rose 52 Mt, because high gas prices pushed some generation from gas to coal, and US coal power rose 85 TWh. The IEA, counting CO2 only, also finds power emissions flat at about 13,900 Mt. Across the whole energy system, energy-related CO2 still rose 0.4% to a record of nearly 38.4 Gt (IEA, Apr 2026). So 2025 was the year clean power met new demand, not yet the year power emissions started to fall.

## Slide 7
02
China: the pivot
Capacity, generation and storage
08
China's wind and solar capacity passed thermal
09
China: thermal output down 0.7%, solar up 39.8%
10
Storage added 112 GW, more than half in China
Notes: Part two is China: capacity, generation and storage, and the role China plays in the world's clean power growth.

## Slide 8
2
China: the pivot
China's wind and solar capacity passed thermal
China's generating capacity at the end of 2025, 3,891 GW by source
Solar
1,202 GW
Wind
640 GW
Thermal
1,539 GW
Hydro
448 GW
Nuclear 62 GW
Solar and Wind 1,842 GW, 47.3%
Thermal 1,539 GW, 39.6%
Wind and solar added each year, GW
120
290
360
430
2022
2023
2024
2025
of China's capacity is wind and solar
47.3%
About 300 GW more
than thermal
of new capacity was renewable
83%
452 GW added in the year
Source: National Bureau of Statistics of China (Feb 2026), China NEA (Jan, Feb 2026). Grid connected
Notes: China ended 2025 with 3891 GW of generating capacity, up 16.1%. Solar reached 1202 GW (up 35.4%) and wind 640 GW (up 22.9%), together 1842 GW or 47.3% of the total, about 300 GW more than thermal at 1539 GW. Annual wind and solar additions have risen four years running: 120 GW in 2022, 290 GW in 2023, 360 GW in 2024 and 430 GW in 2025. Estimates of China's 2025 solar additions vary widely: the official grid-connected AC figure is about 315 to 317 GW, while DC or installed-basis estimates from other bodies run from 370 to 415 GW. This page uses official figures only.

## Slide 9
2
China: the pivot
China: thermal output down 0.7%, solar up 39.8%
Source
Output, full count (TWh)
Change, full count
Change, large plants only
Thermal
6,327
−0.7%
−1.0%
Hydro
1,462
+2.5%
+2.8%
Nuclear
485
+7.6%
+7.7%
Wind
1,128
+13.1%
+9.7%
Solar
1,173
+39.8%
+24.4%
Total
10,575
+4.8%
+2.2%
The large plant count misses much distributed solar, so this report uses the full count.
Source: National Bureau of Statistics of China (Jan, Feb 2026)
Notes: The full count comes from the annual statistical communiqué. The large-plant count covers industrial enterprises above designated size. The two should not be mixed. On the full count, thermal output fell 0.7% and solar rose 39.8%. On the large-plant count solar rose only 24.4%, mostly because distributed solar is left out. Other readings: the China Electricity Council puts coal power output down 1.9%, with coal at 51.1% of generation, and calculates that new wind, solar and bioenergy output equalled 97.1% of the rise in power use. China's total power use was 10,368 TWh, up 5.0%.

## Slide 10
Storage added 112 GW, more than half in China
New storage added worldwide
112 GW
Up 48%
Built in China
54%
The US 16%
Average battery pack price
$70/kWh
Down 45%
Source: BNEF (Dec 2025, May 2026). Battery and other new storage, excluding pumped hydro. Illustrative image
Notes: BNEF counts 112 GW / 307 GWh of new storage added worldwide in 2025, up 48%, with 54% in China and 16% in the US. The IEA and China's National Energy Administration both put the figure at about 110 GW. China's National Energy Administration reports cumulative new-type storage of 136 GW / 351 GWh at end-2025, up 84.3%, with an average duration of 2.58 hours and lithium batteries making up 96.1%. In BNEF's annual survey, stationary storage battery packs averaged $70/kWh, down 45%, the cheapest of any use for the first time. Storage is what moves solar out of the midday hours. BNEF forecasts 158 GW / 459 GWh of additions in 2026. The image is AI-generated and illustrative.

## Slide 11
03
2026: not settled yet
What has changed this year, and what comes next
12
Solar climbs, but gas and curtailment push back
13
Solar installs set for first fall in two decades
Notes: Part three is 2026: progress and headwinds so far this year, and the first signs of slower installation.

## Slide 12
3
2026: not settled yet
Solar climbs, but gas and curtailment push back
World
China
H1
Solar tops 10%
8.9% a year ago
H1
Coal at 49.7%
First time
under half
H1
Utilization slips
Wind 90.9%,
solar 91.4%
July
IEA: coal +1.4%
Gas price shock
End July
Solar passes coal
31.5% of capacity
August
Thermal −4.3%
Steeper than July
Gas prices are the global variable, curtailment the Chinese one.
Source: Ember (Aug 2026), China NEA (Jul, Sep 2026), China NBS (Sep 2026), IEA (Jul 2026)
Notes: The good news: global solar generation reached 1564 TWh in the first half, up 18%, just over 10% of all generation. Between 11 am and 2 pm, solar met more than a quarter of the world's demand. In China, coal generated about 2500 TWh in the first half, 49.7% of the total and the first half-year below half. At the end of July China's solar capacity passed its coal capacity for the first time. Thermal output from large plants fell 4.3% in August. The headwinds: demand is growing faster, with China's power use up 5.3% in the first half and the IEA expecting 3.6% global growth in 2026. The IEA's July mid-year update, as reported in the press, blames higher gas prices on LNG disruption from the war in the Middle East. Gas prices in Asia and Europe reached their highest since the 2022 to 2023 crisis, some markets switched to coal, and the IEA expects global coal power to rise 1.4% in 2026. China's wind and solar utilization slipped to about 91% in the first half, from 94% and 95% for 2025 as a whole.

## Slide 13
3
2026: not settled yet
Solar installs set for first fall in two decades
Actual
Forecast
Global solar, GW
452
595
664
612 (forecast)
−8%
2023
2024
2025
2026
China's new solar, Jan to Jul, year on year
−61%
Global renewable energy investment, 2025
−9.5%
Total energy transition investment still up 8%
Source: SolarPower Europe (Jun 2026), China NEA (Aug 2026), BNEF (Jan 2026). 2026 is a forecast
Notes: SolarPower Europe counts 664 GW of solar installed worldwide in 2025, up 12%, and expects 612 GW in 2026, down 8%, the first decline in more than two decades, mainly because it expects China to fall 24%. The 2023 and 2024 figures of 452 GW and 595 GW are derived from the increases SPE published. This is an installed-capacity count and should not be compared with IRENA's 510 GW or IEA-PVPS's figure of about 690 GW. China added 86.15 GW of solar from January to July, down 61%, and 47.07 GW of wind, down 12%, according to National Energy Administration data reported by PV Tech. Investment is already sending a signal: BNEF puts 2025 energy transition investment at $2.3 trillion, up 8%, but renewable energy investment fell 9.5% to $690 billion, and China's renewable investment fell for the first time since 2013. BNEF's total includes electric vehicles, so it cannot be added to or divided by IEA energy investment figures.

## Slide 14
They decide whether clean power covers all growth again
Three things to watch in 2026
01
Gas
IEA sees coal power up 1.4%
in 2026
02
Curtailment
China's use rate near 91%
03
Storage
BNEF expects 158 GW added
in 2026
Notes: In 2025 clean power met all new electricity demand. Whether it can do so a second year running depends on three things. First, whether the gas shock lifts coal power and power emissions again. The IEA expects coal power to rise 1.4% in 2026. Second, how installation and curtailment change in China now that new wind and solar sell into the market, with utilization already down to about 91% in the first half. Third, how much solar storage can move out of the middle of the day. BNEF forecasts 158 GW of storage additions in 2026.